General  Safety  Information

WARNING

• Use  neutral  detergent  to  clean  the  chain. Do  not  use  alkali-based  or  acid  based

detergent  such  as  rust  cleaners  as  it  may  result  in  damage  and/or  failure  of  the

chain.

• Use  the  reinforced  connecting  pin  only  for  connecting  the  narrow  type  of  chain.

• There  are  two  different  types  of  reinforced  connecting  pins  available. Be  sure  to

check  the  table  below  before  selecting  which  pin  to  use. If  connecting  pins  other

than  reinforced  connecting  pins  are  used,  or  if  a  reinforced  connecting  pin  or  tool

which  is  not  suitable  for  the  type  of  chain  is  used,  sufficient  connection  force  may

not  be  obtained,  which  could  cause  the  chain  to  break  or  fall  off.

Chain

9-speed super narrow

chain such as

CN-7701 / CN-HG93

8- / 7- / 6-speed narrow

chain such as

CN-HG50 / CN-IG51

Reinforced

connecting pin

Chain tool

Technical  Service  Instructions

RD-M751/RD-M571/

RD-M511

SI-5VV0B

Rear derailleur

Chain  length  on  bicycles  with  rear  suspension

The  length  of  A  will  vary  depending  on  the  movement  of  the  rear  suspension.

Because  of  this,  an  excessive  load  may  be  placed  on  the  drive  system  if  the  chain

length  is  too  short.   Set  the  length  of  the  chain  by  adding  two  links  to  the  chain  when

the  rear  suspension  is  at  a  position  where  dimension  "A"  is  longest  and  the  chain  is

on  the  largest  sprocket  and  the  largest  chainring.   If  the  amount  of  movement  of  the

rear  suspension  is  large,  the  slack  in  the  chain  may  not  be  taken  up  properly  when

the  chain  is  on  the  smallest  chainring  and  smallest  sprocket.

Chain

Largest

sprocket

Largest

chainring

3.  Low  adjustment

Turn  the  low  adjustment  screw  so  that  the  guide  pulley  moves  to

a  position  directly  in  line  with  the  largest  sprocket.

Largest

sprocket

Guide  pulley

1

2

In  order  to  realize  the  best  performance,  we  recommend  that  the  following  combination  be  used.

Series

Rapidfire  M9  (Shifting  lever)

Outer  casing

Rear  derailleur

Type

Freehub

Gears

Cassette  sprocket

Chain

Bottom  bracket  guide

XT

SL-M751

DEORE

SL-M511

2

1

Low  adjustment

screw

Silver

TL-CN32 /TL-CN23

6.5mm

Black

TL-CN32 /TL-CN23

7.1mm

• If  it  is  necessary  to  adjust  the  length  of  the  chain

due  to  a  change  in  the  number  of  sprocket  teeth,

make  the  cut  at  some  other  place  than  the  place

where  the  chain  has  been  joined  using  a  reinforced

connecting  pin  or  an  end  pin. The  chain  will  be

damaged  if  it  is  cut  at  a  place  where  it  has  been

joined  with  a  reinforced  connecting  pin  or  an  end  pin.

Reinforced  Connecting  Pin

RD-M751

LX

SL-M571

SIS-SP41

RD-M571

A'

SGS  /  GS

FH-M765  /  FH-M760

FH-M585  /  FH-M580

9

CS-M580

CN-HG73

SM-SP17  /  SM-BT17

CS-M760

CN-HG93

RD-M511

SGS

FH-M530  /  FH-M535

A

Add  2  links  (with  the  chain  on

both  the  largest  sprocket  and

the  largest  chainring)

CS-HG50-9

CN-HG53

4.  How  to  use  the  B-tension  adjustment  screw

Mount  the  chain  on  the  smallest  chainring  and  the  largest

sprocket,  and  turn  the  crank  arm  backward.  Then  turn  the

B-tension  adjustment  screw  to  adjust  the  guide  pulley  as  close  to

the  sprocket  as  possible  but  not  so  close  that  it  touches.   Next,

set  the  chain  to  the  smallest  sprocket  and  repeat  the  above  to

make  sure  that  the  pulley  does  not  touch  the  sprocket.

Smallest  sprocket

2

Largest  sprocket

2

End  Pin

Link  Pin

• Check  that  the  tension  of  the  chain  is  correct  and  that  the  chain  is  not  damaged. If

the  tension  is  too  weak  or  the  chain  is  damaged,  the  chain  should  be  replaced. If

this  is  not  done,  the  chain  may  break  and  cause  serious  injury.

• Obtain  and  read  the  service  instructions  carefully  prior  to  installing  the  parts.

Loose,  worn,  or  damaged  parts  may  cause  injury  to  the  rider.   We  strongly

recommend  only  using  genuine  Shimano  replacement  parts.

• Read  these Technical  Service  Instructions  carefully,  and  keep  them  in  a  safe  place

for  later  reference.

Note

• If  gear  shifting  operations  do  not  feel  smooth,  wash  the  derailleur  and  lubricate  all

moving  parts.

• If  the  amount  of  looseness  in  the  links  is  so  great  that  adjustment  is  not  possible,

you  should  replace  the  derailleur.

• You  should  periodically  clean  the  derailleur  and  lubricate  all  moving  parts

(mechanism  and  pulleys).

• If  gear  shifting  adjustment  cannot  be  carried  out,  check  the  degree  of  parallelism  at

the  rear  end  of  the  bicycle. Also  check  if  the  cable  is  lubricated  and  if  the  outer

casing  is  too  long  or  too  short.

• If  you  hear  abnormal  noise  as  a  result  of  looseness  in  a  pulley,  you  should  replace

the  pulley.

• If  the  chain  keeps  coming  off  the  sprockets  during  use,  replace  the  sprockets  and

the  chain.

• Use  a  frame  with  internal  cable  routing  is  strongly  discouraged  as  it  has  tendencies

to  impair  the  SIS  shifting  function  due  to  its  high  cable  resistance.

• Always  be  sure  to  use  the  sprocket  set  bearing  the  same

group  marks.   Never  use  in  combination  with  a  sprocket

bearing  a  different  group  mark.

• Use  an  outer  casing  which  still  has  some  length  to  spare  even

when  the  handlebars  are  turned  all  the  way  to  both  sides.

Furthermore,  check  that  the  shifting  lever  does  not  touch  the

bicycle  frame  when  the  handlebars  are  turned  all  the  way.

• Make  sure  that  the  gear  shifting  cable  and  the  brake  cable  do

not  obstruct  each  other  during  braking  operations. If  they  do

obstruct,  it  may  interfere  with  braking.

Group marks

Specifications

Rear  Derailleur

Model number

Type

Gears

Total capacity

Largest sprocket

Smallest sprocket

Front chainwheel tooth difference

RD-M751 / RD-M571 / RD-M511

SGS

9

45T

34T

11T

22T

RD-M751 / RD-M571

GS

9

33T

34T

11T

22T

Adjustment

1.  Top  adjustment

Turn  the  top  adjustment  screw  to  adjust  so

that  the  guide  pulley  is  in  line  with  the  outer

line  of  the  smallest  sprocket  when  looking

from  the  rear.

1

2

1

Outer  line  of

smallest  sprocket

B-tension

adjustment  screw

1

1

2

Guide  pulley

1

2

Top  adjustment

screw

5.  SIS  Adjustment

Operate  the  shifting  lever  several  times  to  move  the  chain  to  the

2nd  sprocket. Then,  while  pressing  the  lever  just  enough  to  take

up  the  play  in  the  lever,  turn  the  crank  arm.

When  shifting  to

3rd

When  no  sound

at  all  is  heard

These  Service  Instructions  describe  the  operation  method  when  using  the  Rapidfire  SL-M751/M571/M511  in

combination  with  the  RD-M751/M571/M511  top  normal-type  rear  derailleur.  If  using  in  combination  with  the  RD-M760/

M580/M530  reverse  spring-type  derailleur,  the  operations  and  indicator  displays  will  be  reversed.

Gear  shifting  operation

Both  lever  (A)  and  lever  (B)  always  return  to  the  initial  position  when  they  are  released  after  shifting.   When  operating  one  of

the  levers,  always  be  sure  to  turn  the  crank  arm  at  the  same  time.

To  shift  from  a  small  sprocket  to

a  larger  sprocket   (Lever  A)

To  shift  one  step  only,  press  lever  (A)  to  the  (1)  position.

To  shift  two  steps  at  one  time,  press  to  the  (2)  position.

Lever  (A)  initial  position

To  shift  from  a  large  sprocket  to

a  smaller  sprocket   (Lever  B)

Press  lever  (B)  once  to  shift  one  step  from  a  larger  to  a

smaller  sprocket.

2.  Connection  and  securing  of  the  inner  cable

Operate  lever  (B)  8  or  more  times  to  set  the  lever

to  the  highest  position,  check  on  the  indicator  that

the  highest  position  is  correct,  and  then  install  and

adjust  the  inner  cable.

Tightening torque :

5 - 7 N·m {44 - 60 in. lbs.}

Lever  (B)

Outer  casing

adjustment  barrel

S H M Install  the  cables  so  that  they  still  have  some  slack  in  them  even  when  the

handlebars  are  turned  fully  in  either  direction.

• A  special  grease  is  used  for  the  gear  shifting  cable  (SIS-SP41). Do  not  use  DURA-

ACE  grease  or  other  types  of  grease,  otherwise  they  may  cause  deterioration  in

gear  shifting  performance.

• Grease  the  inner  cable  and  the  inside  of  the  outer  casing  before  use  to  ensure  that

they  slide  properly.

• For  smooth  operation,  use  the  specified  outer  casing  and  the  bottom  bracket  cable

guide.

• Operation  of  the  levers  related  to  gear  shifting  should  be  made  only  when  the  front

chainwheel  is  turning.

• Parts  are  not  guaranteed  against  natural  wear  or  deterioration  resulting  from

normal  use.

• For  maximum  performance  we  highly  recommend  Shimano  lubricants  and

maintenance  products

• For  any  questions  regarding  methods  of  installation,  adjustment,  maintenance  or

operation,  please  contact  a  professional  bicycle  dealer.

Install  the  inner  hole  cover  by  turning  it  as

shown  in  the  illustration  until  it  stops.

Do  not  turn  it  any  further  than  this,  otherwise  it

may  damage  the  screw  thread. In  addition,  if

the  unit  cover  becomes  bent,  it  may  cause  the

unit  cover  to  get  in  the  way  of  the  feed  lever

and  prevent  the  feed  lever  from  operating

correctly.

If  the  feed  lever  does  not  return  correctly,

loosen  the  inner  hole  cover  slightly,  and  then

move  the  feed  lever  and  the  unit  cover  apart

and  check  if  this  improves  the  returning  of  the

feed  lever.

Unit  cover

Outer  casing

adjustment

barrel

Tighten  the  outer  casing

adjustment  barrel  until  the

chain  returns  to  the  2nd

sprocket. (clockwise)

Loosen  the  outer  casing

adjustment  barrel  until  the

chain  touches  the  3rd  sprocket

and  makes  noise. (counter

clockwise)

Feed  lever

Inner  hole  cover

Tightening torque :

0.3 - 0.5 N·m {3 - 4 in. lbs.}

Lever  (B)

Cutting  the  outer  casing

When  cutting  the  outer  casing,  cut  the  opposite  end  to

the  end  with  the  marking. After  cutting  the  outer  casing,

make  the  end  round  so  that  the  inside  of  the  hole  has  a

uniform  diameter.

Installation  of  the  lever

Use  a  handlebar  grip  with  a  maximum  outer  diameter  of  32  mm.

• Install  the  shifting  lever  in  a  position  where  it  will  not  obstruct

brake  operation  and  gear  shifting  operation.

• Do  not  use  in  a  combination  which  causes  brake  operation  to  be

obstructed.

• In  the  case  of  carbon  handlebars,  it  may  be  necessary  to  lower

the  tightening  torque  in  order  to  prevent  damage  to  the

handlebar.   Please  consult  the   bicycle  or  handlebar  manufacturer

regarding  the  appropriate  level  of  tightening  torque  for  carbon

handlebars.

Installation  of  the  rear  derailleur

When  installing,  be  careful  that  deformation  is  not  caused

by  the  B-tension  adjustment  screw  coming  into  contact

with  the  dropout  tab.

Bracket spindle Tightening torque :

8 - 10 Nm {70 - 86 in. lbs.}

Best  setting

The  best  setting  is  when  the  shifting  lever  is

operated  just  enough  to  take  up  the  play  and  the

chain  touches  the  3rd  sprocket  and  makes  noise.

* Return the lever to its original position (the position where

the lever is at the 2nd sprocket setting and it has been

released) and then turn the crank arm clockwise. If the

chain is touching the 3rd sprocket and making noise, turn the outer

casing adjustment barrel clockwise slightly to tighten it until the noise

stops and the chain runs smoothly.

Operate  lever  to  change  gears,  and  check  that  no  noise  occurs

in  any  of  the  gear  positions.

For  the  best  SIS  performance,  periodically  lubricate  all

power-transmission  parts.

Tightening torque :

5 N·m {44 in. lbs.}

Outer  end  cap

Attach  the  same  outer  end  cap  to  the  cut

end  of  the  outer  casing.

5  mm  Allen  key

Connect  the  cable  to  the  rear  derailleur  and,

after  taking  up  the  initial  slack  in  the  cable,

re-secure  to  the  front  derailleur

as  shown  in  the  illustration.

Note:  Be  sure  that  the  cable  is

securely  in  the  groove.

This  service  instruction  explains  how  to  use  and  maintain  the

Shimano  bicycle  parts  which  have  been  used  on  your  new  bicycle.

For  any  questions  regarding  your  bicycle  or  other  matters  which

are  not  related  to  Shimano  parts,  please  contact  the  place  of

purchase  or  the  bicycle  manufacturer.

Pull

5  mm  Allen  key

B-tension

adjustment  screw

Groove

One  Holland,  Irvine,  California  92618,  U.S.A.   Phone:  +1-949-951-5003

Industrieweg  24,  8071  CT  Nunspeet,  The  Netherlands   Phone:  +31-341-272222

Dropout  tab

3-77  Oimatsu-cho  Sakai-ku,  Sakai,  Osaka  590-8577,  Japan

Please  note:  specifications  are  subject  to  change  for  improvement  without  notice.  (English)

©  Jun.  2006  by  Shimano  Inc.    XBC  SZK  Printed  in  Singapore.